## Slide 1
2024 Engines

## Slide 2
Since 1994 significant reductions in PM & NOx
EPA 2010 emissions standard:
  0.2 g NOx
  0.01g Particulate Matter (PM)
Emissions Standards
0.01
0.10
0.2
1.2
2.5
4.0
5.0
1994
1998
2002
2007
2010
NOx [g/hp-hr]
PM [g/hp-hr]
20%
38%
52%
83%
90%
Pollutants

## Slide 3
SCR Selective Catalytic Reduction

## Slide 4: 2007 System Architecture
Oxidation
Catalyst
Diesel
Particulate
Filter
EGR-Cooler
Charge Air Cooler
Urea
Urea Tank
Urea Doser
SCR Catalyst
2010
Slide Courtesy of Detroit Diesel®
Notes: For 2010, the existing 2007 technology is used, with the addition of the Selective Catalytic Reduction (SCR) system.

## Slide 5
= Exhaust
How SCR Works
SCR Device
NOx
PM
NOx
Particulate Matter (PM) is trapped
in the Diesel Particulate Filter
(DPF)
= Diesel Exhaust Fluid
PM
DEF injected into the
exhaust stream
DEF
NH3
DEF solution ‘hydrolyzes’ into
ammonia gas (NH3) which mixes
with the exhaust
Ammonia (NH3) and Nitrogen
Oxides (NOx) react in the catalyst
to form Nitrogen and Water
N2
H2O
Slide Courtesy of Detroit Diesel®

## Slide 6
DEF Diesel Exhaust Fluid

## Slide 7: Diesel Exhaust Fluid
Made from Ammonia (a natural gas by product)
Clear
Biodegradable
Freezing point = 12° F

## Slide 8: Diesel Exhaust Fluid
Material Safety Data Sheet (MSDS)
Hazards Identification “Urea Solution is not Flammable”
First Aid Measures “Wash area thoroughly with soap and water”
Fire Fighting Measures “Urea solution is not flammable”
Transportation Information “Urea solution is not listed by any US or Canadian transportation authority as a hazardous material…”

## Slide 9: DEF Packaging
  Jugs
  Totes
  Pumping Stations

## Slide 10: How Much DEF Will I Use?
Approximately 2% DEF consumption
Every 50 gallons of fuel =
1 gallon of DEF
Notes: We expect about 2% DEF Consumption. Great opportunity to help educate and advise users on consumption rate. Depending on number of 2010 units in a fleet, users can begin planning on actual inventory of DEF that is needed in their shops…..barrel vs. tote, etc.
You can plan to consume about 1 gallon of DEF for every 50 gallons of fuel

## Slide 11
CUMMINS

## Slide 12: Cummins X12
Increased Power Density
  500 HP 1700 ft-lb Torque
Heavy Duty Design
  Replaceable Liners
Advanced VG Turbocharger
Selective Catalytic Reduction Aftertreatment System
Improved Reliability
Notes: The 2010 ISC8.3/ISL9 is built like a heavy duty engine with replaceable wet liners, roller followers, 2 piece steel articulated pistons, by-pass oil filtration and targeted piston cooling. It features an improved Combustion System along with Optimized Calibration for lower Engine Out Particulates.
The cooled-EGR subsystem has set the industry standard for reliability since 2002 and a more robust Electronic Control Module (ECM) on the 2010 ISC8.3/ISL9 not only controls operation of the engine and the new Cummins Aftertreatment System, it coordinates seamlessly with other vehicle systems such as the transmission and brakes. The ISC.3/ISL9 will run at near-zero emission levels, and will achieve comparable fuel efficiency to the ’07 ISC/ISL.
Exceptional performance will be delivered with our proven technology, including High Pressure Common Rail fuel injection, our patented VG Turbocharger, and the new Cummins Aftertreatment System. The High Pressure Common Rail Fuel System delivers an optimum balance of performance, emissions control and fuel economy across the entire operating range.

## Slide 13
SCR Vehicle Impact Custom Chassis
13
65 gal.
Diesel
Fuel
4.5 gal.
DEF
Notes: 13
DEF tanks will always be located on the LH side of the vehicle.

## Slide 14: Cab Controls Gauges and Warning Lamps
Rear Air pressure
Voltage
Tachometer
Speedometer
Fuel
Oil pressure
Front Air Pressure
Coolant Temperature
Transmission Oil Temperature
Display Module

## Slide 15: Cab Controls Gauges and Warning Lamps
Rear Air pressure
Voltage
Tachometer
Speedometer
Fuel
Front Air Pressure
Display Module
CEL (Check Engine Light) will prevent engine from conducting a Regen